| Item No | Description of Supplies | Qty | Unit of Measure | Unit Price | Total Price |
| --- | --- | --- | --- | --- | --- |
| 1 | Digital earth megger for earth resistance measuring during repairs and installations in the plants, R&B and branches-WPD | 01 | Item |  |  |

Specification and Compliance Sheet

| Item no | Technical Specification Required | Provide Specification to be Offered and state compliance | Technical literature on specification offered in column c |
| --- | --- | --- | --- |
| a | b | c | d |
|  | Earth Merger: JSDZ905 |  |  |
| 1 | Function 2/3/4 –pole measurement for earth resistance, soil resistivity, earth voltage, AC voltage |  |  |
| 2 | Power supply 8.4VDC, 2600mAh rechargeable lithium battery |  |  |
| 3 | Measurement range Earth resistance: 0.00 Ω – 30.ook Ω Soil resistivity: 0,00 Ωm -9000k Ωm Earth voltage: 0V -600V |  |  |
| 4 | Measurement mode Precise 4-pole measurement , 3-pole measurement, simple 2 pole measurement |  |  |
| 5 | Measurement method Earth resistance: rated current change pole method, test current 20mA max Soil resistivity:4-pole method Earth voltage: average rectification (between P(S)-ES) |  |  |
| 6 | Open-circuit test current: 40VAC |  |  |
| 7 | Test Voltage Wave: sine wave |  |  |
| 8 | Electrode Distance Range: 1m -100m |  |  |
| 9 | Shift Earth resistance: 0.00 Ω -30.00k Ω automatic shift Soil resistivity: 0.00 Ωm -9000k Ωm automatic shift Backlight: controllable white screen backlight, suitable for dim places |  |  |
| 10 | Dimensions LCD frame Dimensions 128mm x 75mm LCD Window Dimension 124mm x 67mm Meter Dimension: (L*W*H) 280mm x 260mm x160mm |  |  |
| 11 | Standard Test Wire: 4 wires Red 20m Black 20m Yellow 20m Green 10m |  |  |
| 12 | Auxiliary ground rod 4 wires: Ø10mm x 150mm |  |  |
| 13 | Measurement Rate: Voltage to earth: 3 times per second Earth resistance, soil resistivity: 5 times per second |  |  |
| 14 | Measuring times Over 5000 times (short circuit test, interval time should be at least 30 seconds) Circuit voltage: below 600VAC |  |  |
| 15 | Communication interface: USB interface, software monitoring, storage date can be uploaded computer, saved or printed. Communication wire: one piece USB communication, length 1.5m |  |  |
| 16 | Data storage 300 sets, MEM symbol storage indicator, flash display FULL symbol indicate storage full |  |  |
| 17 | Alarm Function Measurement value exceeds alarm setting , the alarm should sound |  |  |
| 18 | Auto –shut off Automatically shut down after 10minutes of power Working temperature: -100C -400C Humidity 60 -80%rh Storage temperature: -200C – 600C Humidity 50 -70% |  |  |
| 19 | Overload protection: Measuring Earth resistance : between each interface of C(H) –E, P(S)-ES, AC 280V/3 seconds |  |  |
| 20 | Packaging: water proof hard plastic case with the megger, Polyster bag with all the components: 4 copper test earth rods 5 copper testing cables Earth megger Charger USB cable Earth megger Batteries Software CD Instruction manual |  |  |
| 21 | Warranty: 12 months from the date of acceptance |  |  |